## Slide 1: Negative numbers: Week 10 Lesson 1

## Slide 2: How to represent negative numbers
There is a fixed number of bits in a processor to store data:
32-bit
64-bit
At GCSE you only look at 8-bit numbers, but the principle is the same.
How many positive whole number values can be stored:
in 4 bits?
in 8 bits?
So, how are negative numbers represented in 8 bits?
Sign and magnitude
Two’s complement

## Slide 3: Sign and magnitude
The most significant bit is the ‘sign bit’:
1 = minus and 0 = plus
–27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 
1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 
– | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 
 |  |  |  | 8 | 4 |  | 1 | = –13
Conversion to denary is the same: just add up the values.
Remember that the number is now negative.
If the sign is 0, it is a positive number.

## Slide 4: The problems with sign and magnitude
Both 1000 0000 and 0000 0000 represent 0.
It wastes one binary code.
Addition doesn’t always work.
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | = | +7 | 
1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | = | –5 | +
1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | = | -12 | 

## Slide 5: The alternative: two’s complement
The most significant bit is a minus number as well as a sign bit.
–27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 
1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 
–128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 
-128 |  |  |  | 8 | 4 |  | 1 | = –115
The largest positive number that can be represented is
0111 1111 (i.e. +127)
The largest negative number that can be represented is
1000 0000 (i.e. –128)

## Slide 6: The same sum in two’s complement
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | = | +7 | 
1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | = | –5 | +
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | = | +2 | 
And there’s only one way of representing 0:
0000 0000

## Slide 7: Shifts: arithmetic – with negative numbers
Left-shift |  | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 |  | (decimal 23) | 
 | = | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | (decimal 46) | 
Right-shift |  | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 |  | (decimal -105) | 
 | = | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 |  | (decimal -53) | 
This has the effect of multiplying by 2.
A new 0 is shifted in.
This has the effect of dividing by 2.
The MSB value is always maintained; in this example a 1 is inserted.
Arithmetic right-shift best for signed two’s complement since this retains the MSB (i.e. sign) value.

## Slide 8: Shifts: logical
Left-shift |  | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 |  | (decimal 23) | 
 | = | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | (decimal 46) | 
Right-shift |  | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 |  | (decimal 23) | 
 | 0 |  |  |  |  |  |  |  |  |  |  | 
 | = | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 |  | (decimal 11) | 
This has the effect of multiplying by 2.
A new 0 is shifted in
This has the effect of dividing by 2.
In a logical shift a 0 is always inserted.
Logical shifts, which always copy in a 0, are ideal for unsigned binary numbers